Multi-scale adjoint tidal and storm surge modelling with Thetis
Simon C Warder, Matthew D Piggott

Overview

The Thetis model, developed under PRISM in a collaboration between ESE, Maths and Computing, is used extensively for a variety of coastal ocean modelling applications. A key application area for Thetis is tidal modelling, for example in tidal energy or sediment/pollutant transport problems. More recently, Thetis has been employed for the modelling of storm surges, which are caused by low atmospheric pressure and strong winds driving water against the coastline. Since tide-surge interaction plays an important role in storm surge dynamics, accurate tidal modelling is therefore a prerequisite for accurate storm surge modelling, and also feeds into the modelling of other coastal hazards.

Two-dimensional modelling via the shallow water equations (under the Boussinesq and hydrostatic assumptions) is often considered sufficient for tidal and storm surge modelling on large horizontal scales (e.g. on the scale of the continental shelf). However, there are a variety of coastal ocean applications requiring the representation of three-dimensional and/or nonhydrostatic effects. Examples include high-resolution modelling of tidal turbine arrays, or the modelling of dispersive waves. One aim of this project is the further development and testing of 3D and/or nonhydrostatic modelling in Thetis.

A second aspect of this project is in the continued development of Thetis as an uncertainty quantification tool for tidal and coastal hazard modelling. Since accurate tidal modelling depends on a number of uncertain model inputs, including bathymetry and a parameter governing bottom stress due to sea floor roughness, frameworks for sensitivity analysis, uncertainty quantification and model calibration are essential to the intelligent application of a tidal model. Furthermore, since storm surge modelling requires additional model inputs (atmospheric pressure and wind velocities), which are typically highly uncertain in a forecast scenario, a robust uncertainty quantification framework takes on even greater importance.

In particular, there are two existing applications of Thetis which will be extended within this project. Firstly, the adjoint available within Thetis facilitates a gradient-based uncertainty quantification approach (in contrast with ensemble methods typically employed in operational modelling). Preliminary work has been completed in the use of Thetis and its adjoint for storm surge uncertainty quantification [1], and this project aims to extend this work, further strengthening Thetis as an uncertainty quantification tool. Secondly, the adjoint facilitates an efficient gradient-based approach to model calibration. A preliminary tidal modelling case study [2] has shown that model parameters calibrated via the adjoint in Thetis can be successfully applied to independent numerical models. This can be applied to both tidal and storm surge modelling. This project will perform further work, testing the applicability of calibrated parameter sets for a broader set of modelling case studies and numerical models. This aspect of the proposed work aims to increase the impact of Thetis in the wider coastal ocean modelling community.

Alignment with PRISM strategy

Retention of key staff: This provides bridge funding for Simon Warder. He has experience contributing to and applying the Thetis model in storm surge and tidal contexts, and in the application of adjoint-based techniques for sensitivity analysis, uncertainty quantification and model calibration.

Longer-term research: The developments described in this proposal will broaden the use of Thetis within a wide range of coastal ocean modelling applications. This will raise the impact of PRISM research, and facilitate the use of Thetis in a broader range of future research projects.

[1] S. C. Warder, K. J. Horsburgh, and M. D. Piggott. Adjoint-based sensitivity analysis for a numerical storm surge model. Ocean Modelling, Submitted 2020.
[2] S. C. Warder, A. Angeloudis, S. C. Kramer, C. J. Cotter, and M. D. Piggott. A comparison of Bayesian inference and gradient descent approaches for friction parameter estimation. Ocean Modelling, submitted 2020.